______________________________________          

            TATUNG EINSTEIN

              ARCHIVE.COM

                 G6GLP
______________________________________            
 
OVERVIEW
--------
ARCHIVE  was  produced to allow  rapid 
re-loading  of TNC battery backed  RAM 
data,lost  as  a  result  of  software 
lockup.   A disc file of parameters is 
held for up-loading into the TNC. This 
file must be present on  the  disc  in
the  default drive.

PROGRAM BACKUP
--------------
It  is essential before  running  this 
package,  that  a backup is  made.  In 
order to back  up   the   data   file, 
( ARCHIVE.TNC) the following procedure 
needs to be carried out.

From  the  System disc,  load and  run 
COPY.  At  the *  prompt,  insert  the 
source  disc  in  drive  0.  Type  the 
following:

*0:*.TNC TO 0:<V>  <enter>

Follow   the  instructions  given   on 
screen.

The program file,  (ARCHIVE.COM),  and 
this  document file (ARCHIVE.DOC)  can 
be backed up in the normal way.

HARDWARE REQUIREMENT
--------------------
In order for ARCHIVE to operate in the 
correct   manner,   the  TNC  must  be 
running 1.1.3 software and  configured 
for 1200 baud computer interface.

OPERATION
---------
To  run  the  program,   type  ARCHIVE 
<enter> You will be presented with the 
main  menu.  If this is the first time 
the program has been run you will need 
to  save  your  TNC parameters to  the 
data file.  Type  S  to initiate this.

If,  when running ARCHIVE,  the   main
menu  does not appear,  then the  data
file  is not on the default drive. Use 
of the  ESC key will take the  program 
back   one   level  each  time  it  is 
pressed,   but  will  only have effect 
when  the program is  awaiting  input. 
To  load  the  TNC   with   previously
saved   data,   run  ARCHIVE  and   in 
response to  the main menu,  type   L.
When  complete,  the main menu will re 
appear,    and    the    prompt   will 
disappear.
Press ESC to exit to DOS.

During  the  course  of   Saving    or
Loading    data,      the      message
'WORKING'    should  appear.   If  the 
message  'FAIL'  persists,  then it is 
suggested  that  your  TNC  baud  rate 
and  computer connections be  checked. 
It  will also be necessary  to   reset
the computer.

Please   feel   free   to   distribute
this  package to anyone who  can  make 
use   of   it.   Any  suggestions   or 
improvements  should be  forwarded  to 
G6GLP.