__________________________________________________________________________

MLOAD  - a multi-file hex load utility for CP/M
__________________________________________________________________________


Written by Ron Fowler, Fort Atkinson, Wisconsin.  This  documentation  was
extracted from the source file (MLOAD21.ASM), with trivial modifications.

This program is a replacement for the CP/M  "LOAD"  program.  Why  replace
"LOAD"? Well... LOAD.COM has a few deficiencies. For example, if your  hex
file's origin is above 100h, LOAD.COM prepends blank space to  the  output
file to insure it will work as a CP/M transient. It cares not if the  file
is not intended as a CP/M transient. It also doesn't like hex records with
mixed load addresses (for example, one that loads below a previous  record
-- which is a perfectly legitimate happenstance). Also, LOAD.COM can  load
only one program at a time, and has no provision for a load  bias  in  the
command  specification.  Finally,  there  is   no   provision   for   user
specification of output file name.

Hence, this program....

Command syntax is as follows:

MLOAD [<outnam>=] <file1>[,<file2>...] [bias]

where:

<outnam> is the (optional!) output file name (only the drive
spec and primary filename may be specified; the output filetype
is derived exclusively from the 3-byte string at 103h within
MLOAD).

<filen> are the input files.  <file1> may specify an extension,
in which case it is assumed to be a binary file (starting at
100h).

<bias> is the offset within the saved image to apply when
loading the file.


MLOAD with no arguments prints a small help message  --  this  message  is
also printed whenever a command line syntax error occurs.

Filenames may contain drive specs, and must not contain  wildcards.  Input
filenames must be separated by commas, and a space is required between the
last filename and the optional  bias.  Note  that  ZCPR2-style  drive/user
notation may be used in all file specifications
(e.g., "B3:MYFILE.COM, "A14:MDM7.HEX").

A load information summary is printed at the successful conclusion of  the
load. Any errors in loading will generally include the name of the file in
question.

If no output filename is specified, it will  be  derived  from  the  first
input filename, with filetype of  'COM'  (this  default  filetype  may  be
patched directly into MLOAD  via  DDT  --  its  location  is  at  103h  in
MLOAD.COM). Note that a command line  of  the  form  "C:=<filename>"  will
place the output file on the "C" drive with the same primary  filename  as
the first input file.

In its simplest form, MLOAD's syntax is identical to LOAD.COM; thus  there
should be no problem  in  learning  to  use  the  new  program.  The  only
significant difference here is that, under LOAD.COM, all files are  output
starting at 100h, even if they originate elsewhere. MLOAD outputs starting
at the hex file origin (actually,  the  first  hex  record  specifies  the
output load address). The bias option may be used to override this.

An example should clarify this. Suppose you have  a  file  that  loads  at
1000h. LOAD.COM would save an output file that begins at  100h  and  loads
past 1000h (to wherever the program ends). MLOAD will save an output  file
starting from 1000h only. If, for some reason you need the file  to  start
at 100h in spite of its 1000h origin (I can think of several circumstances
where this would be necessary), you'd have to specify  a  bias  to  MLOAD.

Thus, using this example, "MLOAD MYFILE 0F00" would do.

Note that this program re-initializes itself each time it is run. Thus, if
your system supports a direct branch to the TPA (via  a  zero-length  .COM
file, or the ZCPR "GO" command), you may safely re-execute MLOAD.

Please report any bugs, bug fixes, or enhancements to me at:

"Fort Fone File Folder" RCPM/CBBS
Fort Atkinson, Wisconsin
(414) 563-9932 (no ring back)

       Ron Fowler
       03/08/84
*}TASCODE2$$$ÿÿtastable.bin",â,C,  -–