_____________________________________________________________________

                          UNLOAD.COM   &  MLOAD.COM
     _____________________________________________________________________


     In order to transmit  a  .COM  machine  code  program  or  any  other 
     non-ASCII  file via a modem or packet radio TNC requires the file  to 
     be in ASCII format ie only characters 32 to 127 are  permissable.  If  
     the   modem  receives  characters outside this range,  its  operation 
     can be upset.

     UNLOAD will take any .COM file and convert  it  into  the  equivalent 
     string of HEX codes in ASCII format  in  a  new  file  which  can  be 
     transmitted via your communications  link.  MLOAD  will  reverse  the 
     procedure at the other end and regenerate the original .COM file.

     To use type in UNLOAD FILENAME [ENTER]
                    MLOAD  FILENAME [ENTER]

     _____________________________________________________________________