UKM7EIN2
                                   ========

UKM7EIN2 replaces UKM7EIN1 both of which are Tatung Einstein variants of  UKM7
v1.0. The original suite of files appear in CPMBBUK volume 50 and were updated
by  me  in  volume 70 and called UKM7EIN1. The purpose of these  changes  were
initially to replace unreliable code and provide a default protocol from boot.
The  latest  version allows the user to change all the  usual  comms  protocol
settings  from within the program aswell as toggle the status of the RTS line.
Owners  of  Demon or Voyager modems using this facility will now  be  able  to
control  their  On/Off  line status. This version also  includes  routines  to
signal  a Demon modem so that the Baud rate set for comms is also set  on  the
modem  when  going  "On  line". I may yet include  loop  disconnect  auto-dial
routines.  The unreliable code referred to earlier is now completely  reliable
and  files have been transferred successfully between a PC compatible  running
PRO-COMM  and  an  EINSTEIN  running UKM7EIN2 at 9600  Bauds  (direct).  I  am
grateful  to  Neil  Imrie  for his indispensable help in  creating  this  last
version.  The auto-answer message which presently reads "FRED BLOGGS"  can  be
patched at address 123-158H inclusive. First name should be separated from the
surname  by  a  semi-colon  (3bH) and the string should  be  terminated  by  a
CR(0dH), LF(0aH), and a zero(00H). Advise on how to do this is available  from
many sources including the UK Einstein User Group (0473-49507).

Dave West
Aylesbury
18/05/87