RUNNING PUBLIC DOMAIN SOFTWARE ON THE EINSTEIN         ( Andrew Wilmot )
**********************************************

 There is a great deal of Public Domain software available ( i.e. free )
from Bulletin Boards, Interest Groups, etc. A lot of the programs
written under CP/M will run without modification on the Einstein. This is 
because the Einstein's Operating System is semi-CP/M compatible. I say
"semi" because Tatung have deviated from the standard in some quite
important respects. However these anomalies can be adjusted in most cases.
 Two interesting CP/M P.D. programs are DU.COM and FINDBAD.COM. The first
is a complete disc sector editor, allowing you to examine any part of the
disc and even modify it if you want to. It is a very comprehensive utility.
The second will work its way through the disc and let you know if you have
any bad sectors, but more importantly, will tell you where they are.
 Neither of these will work on the Einstein without modification. I have
detailed below, the patches that are necessary to get both programs up and
running. The first thing to do is to load the unmodified program into
memory by typing LOAD DU.COM ( or FINDBAD.COM ). Make a note of the number
of blocks used. Now drop into MOS by typing MOS <E>. Using the M command,
alter the memory locations as shown in the sections below. When you have
finished type . <E>, then G <E> and you are back in DOS. To save the
patched program, type SAVE N DU-EIN.COM ( or FBAD-EIN.COM depending on which
program you have patched ). N is the number of blocks that the program
occupied.
 Both DU.COM and FINDBAD.COM are available from:

  TUG 11 on 021 444 1484  ( if you have a modem )

  CPMUG  on 0753 868196   ( and you need to be a member )

  UKEUG  contact JIM ELLACOTT ( see the back of the magazine )




 The Public Domain Utility DU.COM by Ward Christensen.
 *****************************************************

 The patches to be made are as follows ( hex values ):

 (1)   #0181   #00  was    #22
       #0182   #00         #2B
       #0183   #00         #14

       #142A   #C5  was    #CD
       #142B   #E1         #00

      
  This last patch allows the code at #142A to run rather than calling the 
BIOS SECTRAN function vector #FA30. Instead of performing this physical to 
logical sector routine, it simply makes physical = logical (true for Einstein).
  The original program was written to put the vector at #142B,#142C. On the 
Einstein this BIOS function is corrupted to be a re-entry to MOS.



(2)       #1274   #7F   was      #15 ... inhibits CNTRL - U
          #127E   #19            #08 ... DEL instead of CNTRL - H
          #12C2   #19            #08 ... DEL instead of CNTRL - H
          #1309   #00            #3E ... prevents the characters
          #130A   #00            #5E     ^ and U being printed when
          #130B   #00            #CD     deleting past the prompt 
          #130C   #00            #3A      "
          #130D   #00            #13      "
          #130E   #00            #3E      "
          #130F   #00            #55      "
          #1310   #00            #CD      "
          #1311   #00            #3A      "
          #1312   #00            #13      "



   This patch allows the Einstein DEL key to be used. In addition a
 few screen control patches have been made for the Einstein's semi-
 compatible FDOS.



 The Public Domain Utility FINDBAD.COM
 *************************************

 The patches to be made are as follows ( hex values ):


       #01C8   #00  was    #22
       #01C9   #00         #BF
       #01CA   #00         #03

       #03BE   #C5         #C3                                   
       #03BF   #E1         #00
       #03C0   #C9         #00
      
  The original program was written to put the BIOS SECTRAN vector
 at #03BF,#03C0. On the Einstein this BIOS function has been corrupted to 
 be a re-entry to MOS.
t the BIOS SECTRAN vector
 at #03BF,#03C0. On the Einstein this BIOS function has been co