SCROLLING  VRAM


      The  80-column  screen  is divided  into  8 pages,  numbered  0 - 7  and
accessed  through ports 40 - 47 (hex.) respectively.  The characters are  held
in a one-dimensional array in VRAM starting at the top left of the screen  and
moving  across the row, then across the next  row down, and so on. The  screen
offset is given by

            screen offset = row * (chars per row) + column

noting that the first row and column are numbered zero.

      The  first character  on the  screen can  be at  any  address  in  VRAM,
although in normal scrolling only addresses with a zero last hexadecimal digit
are encountered. The offset of a character in VRAM is therefore given by

            VRAM offset = screen offset + start offset [ - 800H ].

The  VRAM is 2 Kbytes ( = 800H ) in size  so if the result  is negative,  800H
must  be added,  because the  VRAM array  is circular.  When the screen  start
address  is in the  middle of VRAM,  the end of  the array wraps round  to the
start of  VRAM. Thus  at most times the bottom portion of the screen is at low
VRAM  addresses and  the top portion  at high addresses.  This means  that the
whole screen can be scrolled instantaneously by changing the start address (as
Paul Burgess showed) but it also means that it is not possible to scroll parts
of the screen in this way unless MOS is altered.

      Finally the VRAM address is obtained by

            VRAM address = VRAM offset + 4000H.

The high byte is placed in the C register and the low byte in the  B register:
that  is the  bytes are  switched before  passing to  the  machine  code  port
instructions.

      It  will be apparent that the  VRAM size of  2048 bytes is not an  exact
multiple  of the line length  and in fact the  screen effectively wraps  round
after  780H ( = 24 * 80 ) bytes.  This leaves  80H bytes for a menu line  (has
anyone  managed to display the last 30H bytes?). The menu line appears at  the
bottom  of the screen and stays there when the screen is scrolled, because  it
is  actually scrolled in VRAM  and held just before  the start address of  the
screen.

      The parameters of the screen are stored as follows:

            address (hex.)      bytes

               FB4A               1              cursor column
               FB4B               1              cursor row
               FB4C               2              screen start offset in VRAM
               FB4E               1              used by 40-column screen
               FB4F               1              characters per row

The  values read will be the  values at the time of  access and are liable  to
change in the process of display on the screen (alternatively MCAL  D1H,ZSCURS
can  be used).  For further  information on  screen manipulation  try the  BBC
Advanced User Guide.

      One  useful item  which Tatung  omitted from  the MCAL  descriptions  is
direct  cursor addressing. This  moves the  cursor to  any specified  position
using  ASCII code 29 ( = 1DH = CTRL-] ) and is essential for customising  CP/M
programs.  The control code must be followed  by the column first and the  row
next. Try it in MOS: column 2 is of course input as CTRL-B from the  keyboard.
For column 0 try one of the (unset) function keys.

      The  listing shows a  demonstration program to  illustrate these  points
written  in Nevada  Pascal  and  machine  code.  This  combination  shows  the
interface better than most. The only unusual Pascal instructions are MAP which
assigns an absolute address to a pointer and '+' which concatenates arrays. No
optimisation has been carried out since this is liable to make the code harder
to follow.

      The  basic loop is  quite simple and  is illustrated  in procedure  time
which  outputs the  elapsed time  to a  portion  of  the  menu  line.  Writing
backwards facilitates the coding. Procedure moveline copies a line in a window
to  the next line up  or down. The same  loop is used  but additional code  is
required to check for page changes and wrapping. However the main complication
is that the sequence of instructions carried out by INI and OUTI is different,
in contradiction to the Z80 manual: can anyone explain?

      It  is helpful to follow  the changes in the  registers when looking  at
machine  code: compile the  program with the  first byte of  code replaced  by
0FFH.  When the program  stops replace the original value using  M (at the  PC
address). Use T to inspect the code and E to move to the next instruction. The
screen  display is  of course  destroyed.  If the  program  seems  a  bit  too
complicated,  you can always cheat by using CTRL-L ( 012H ) first. After  this
control  code, the screen start address is zero and no wrapping occurs  (until
you produce line feed on the bottom line!).

      The  information given here is mainly based on deduction plus trial  and
error. If I have missed any points, further elaboration would be welcome.


C. P. WALLIS.
23/1/86.