SERIAL 8056 PRINTER

                FOR DOS 1.31 AND DOS 80 ONLY

      The program SRL8056.COM has been designed so that the serial 
printer called 'SERIAL 8056 COMPACT PRINTER' can be used with the Einstein.
The program arranges that comands to output to the printer are routed to the 
232 port instead of the Centronics port, otherwise the DOS v1.31 opperating 
system is not affected. Other serial printers which use the asynchronous Clear
to Send protocol should also work provided that the same Baud Rate setting of
1200 Baud is specified for the printer.  N.B. serial printers which use the XON
/XOFF protocol will not work in conjunction with this program, such printers 
will need to use the program SRLXNXFF.COM .

      To re-configure the DOS 1.31 operating system for the SERIAL 8056 printer
simply type
                         SRL131        for DOS 1.31
                         SRL801        for DOS 80

The operating system on the disc containing the program SRL??? is already 
configured for the SERIAL 8056 Compact Printer. Also on this disc is the 
program SYSGEN which enables an operating system on one disc to be copied onto
another without affecting any of the files already present on the receiving 
disc. To run SYSGEN simply type SYSGEN. The screen display tells you what to do

N.B.  The screen dump to printer command (ctrl-A) is NOT implemented

This re-configured operting system for the serial printer is compatible with 
the following System Software
       1.   The BATCH processing system
       2.   The Amstrad CP/M emulator
version AMRUN131.COM for DOS 1.31
version AMRUN80.COM  for DOS 80
       3.   If you wish to use the Console Command editor with the serial 
printer DO NOT use the CTRL-R or CTRL-S comands

       For anyone who wishes to make up their own lead the details are:

       EINSTEIN                                   SERIAL 8056

       Pin 3 (TxD)                                Pin A04
       Pin 2 (CTS)                                Pin A07
       Pin 1 (ground)                             Pin B04
                     No other connections are required

       The diagram of the RS232 socket on the Einstein is shown in the book
'An Introduction to the EINSTEIN'.

       The diagram of the 16 pin connector for the printer is in the booklet
which is supplied with the printer.

       These 2 programs are not protected because it is believed that you will
be able to make better use of them in unprotected form. Please remember however
that we make our living by writing software, so don't rip it off! After all it
is sold at a very low price.

       Please note that this alteration to the operating system does not
affect the original copyright. The original copyright remains unchanged.